## Slide 1: Oregon State University NASA USLI Progress Report Mark Bereza Joseph Struth Kevin Turkington 11/30/2017

## Slide 2: Mission Overview
Aerodynamics/Recovery System:
Drogue Velocity:
75 ft/s
Time delay before motor
section drogue ejection
Main Deploys at
750 ft AGL
Payload section drogue ejects first
Payload and motor sections separate at apogee
Payload rover ejects
Notes: General Overview

## Slide 3: Overview: Rocket Design
45.2 lbs at launch
5” diameter
116” length
Notes: General Overview

## Slide 4: Overview: Rover Payload
Notes: Component Overview: Rover

## Slide 5: Overview: Rover Payload
Rocket body identification: GPS and ultrasound
Collision avoidance: ultrasound
Absolute and relative direction: IMU w/ nine degrees of freedom:
Magnetometer w/ X,Y,Z
Accelerometer w/ X,Y,Z
Gyroscope w/ X,Y,Z
Wheels can move independently forwards and backwards
Three levels of movement algorithms
Notes: Component Overview: Rover

## Slide 6: Overview: Rover Software
Three movement algorithms of decreasing complexity:
  SLAM: determine location of rocket body and path find a route at least 5 feet from the rocket body
  Obstacle avoidance: use combination of IMU and sonar sensors to avoid obstacles and steep elevation changes while moving away from rocket body
  Basic movement: face away from rocket body and move until rover no longer can.

## Slide 7: Overview: Rover Software, Cont.

## Slide 8: Overview: Avionics Data Logging Module
Avionics Sensors
RF Transceiver
GPS
Power Supply
GPS Antenna
RF Antenna
Micro Controller
Responsible for collection of in-flight sensor data.
Data collected from sensors via serial communication, stored in flash memory, and displayed post-flight on team website.
Notes: Component Overview: Avionics

## Slide 9: Overview: Website
One place for all USLI team information
  Contact information
  Photos
  Team role
Provides deliverables for NASA
  Presentation slides and documents for PDR, CDR, FRR, etc.
Provides educational outreach information
Notes: Component Overview: Website

## Slide 10: Stumbling Blocks: General
PDR areas of improvement:
  Safety (got 40% of total points)
  Solution: increased focus on safety by all team members, rewrite environmental safety bullet points in document (misunderstood expectations)
Notes: Component Overview: Avionics

## Slide 11: Stumbling Blocks: General, Cont.
Underclassmen leaving or losing interest:
  Result of this term being almost entirely designing, documentation, and planning
  Solution: Now that parts have arrived and more hands-on work is available, we can begin trying to reach out to underclassmen again and promise them more fun work to do than simply attending design meetings

## Slide 12: Stumbling Blocks: Rover
ROS learning curve is greater than anticipated.
  Solution: Work on simulations, using Brad’s ROS simulation code from his robotics class.
Waiting to start development until testbed was completed.
  Solution: Testbed finished at the end of November.
Notes: Component Overview: Avionics

## Slide 13: Stumbling Blocks: Avionics
Waiting for parts to arrive, due to lack of funding hindered development.
  Solution: Grant approved 11/28/17
Sensors were unknown , which hindered development.
  Solution: Sensors decisions finalized by avionics sub-team lead on 11/03/17.
Development could not start until sensors delivered.
  Solution: Started research on serial communication libraries.
Notes: Component Overview: Avionics

## Slide 14: Stumbling Blocks: Website
Details for features and website design.
  Solution: Discussed with team leads during October. Design finalized before PDR was due to NASA.
Making web development work available to underclassmen USLI team members.
  Solution: Github issues.
Notes: Component Overview: Avionics

## Slide 15: Progress: General
PDR score sheets are in…
  We are top 20% in the competition
  Equates to 11th out of 50 teams!
Contributions:
  Kevin Turkington: Website/Verification Plan
  Joseph Struth: Website/Verification Plan
  Mark Bereza: Verification Plan/Software Design
Notes: Updates/Progress: General

## Slide 16: Progress: Rover
Setup Raspberry Pi playground online with Raspbian installed
Did some ROS tutorials for practice
Setup ROS on Pi and begin creating simulations.
Notes: Rover Progress

## Slide 17
Progress: Rover Software Design Decisions
Software Framework
  ROS (Robot Operating System)
  MRPT (Mobile Robot Programming Toolkit)
  MRDS (Microsoft Robotics Development Studio)
Operating System
  Ubuntu
  Raspbian
  Windows 10 for IoT
Languages
  C++
  Python
  C#
Notes: Rover Progress

## Slide 18: Progress: Rover Simulations
Notes: Progress: Rover

## Slide 19: Progress: Rover
3D printed parts: Motor mounts, Sonar mounts, Ball caster for back wheel.
Laser Cut: Plywood 7/32”
Notes: Rover Progress

## Slide 20: Progress: Data Logger
Adafruit Python IO Library (made for BeagleBone Black):
  Supports GPIO, PWM, ADC, I2C, SPI, UART
Development plan: Start with one sensor at a time reading and storing data, integrate more as they arrive.
Final system ready for subscale
Notes: Avionics Progress

## Slide 21: Progress: Website
Set up website on osuusli.com domain name
USLI team information sidebar created
Final Website designs implemented to site
Posted PDR and proposal documents on team website
Notes: Component Overview: Avionics

## Slide 22: Progress: Educational Outreach
First Outreach Event:
Silver Crest School (K8) - Built and launched model rockets (A-motors) on the OSU campus after a presentation about rocketry. Provided a tour of the local AIAA chapter lab space.
Second Outreach Event: Philomath Middle School (K6-7) - Gave a presentation about rocketry and STEM at OSU. Conducted a Question and Answer period. Decorated and launched model rockets!
Future Outreach Events:
December: Sunset High Schools, Walker Middle School 13th (All Day)
All Later Months:
  Coordinating schools with alumni
information and availability.
Notes: Updates/Progress: Educational

## Slide 23: Looking Forward: General
Upcoming Events:
  CDR Q&A 12/1/17 @ 11:00 AM (next Friday)
  Formal Design Review 12/1/17 @ 5:00 PM (next Friday)
  Subscale rocket completion 12/8/17 (end of term)
  Critical Design Review (CDR): January
Create Latex template for CDR document:
  Assist team in compiling document and learning Latex.
Notes: Looking forward

## Slide 24: Looking Forward: Rocket
Ejection testing
  5” mockup airframe currently being designed
  Will determine final black powder loads/reliability
Subscale testing
  Before Critical Design Review
  4” diameter launch vehicle
Full scale testing
  Before Flight Readiness Review
Notes: Looking Forward /Current Status

## Slide 25: Looking Forward: Rover Payload
Testing Procedures
Slope and Soil Texture
Obstacle Course
Dust and Particle Tolerance
Inter-System Interference
Power Consumption
ARLISS: University of Tokyo, 2014
Notes: Looking Forward/ Current Status